## Slide 1: IBM System Storage DS3000 and DS4000 Service Enhancement: IBM Remote Support Manager for Storage
Notes: Charts containing the detailed information have speaker notes –

## Slide 2: The focus of today’s discussion
IBM
Remote Support Manager
for Storage
Manage and analyze alert notifications for the DS3000 and DS4000 families of storage subsystems with accuracy, efficiency and cost effectiveness

## Slide 3: RSM for Storage can Help
RSM for Storage can help to create enhanced value
Faster response time to alerts
Detailed information on each alert for error analysis and accuracy
Manages up to 50 storage systems per implementation with no annual fees
Customer control of remote access and email notifications of changes in system status.
Error Analysis
Management
Monitor up to 50 storage systems
Faster Response
Enhanced Value
Lower IT Costs
RSM for Storage
Detailed information for each alert to improve error analysis and accuracy
Security

## Slide 4: RSM for Storage - Overview
A software package that installs on customer supplied components
  Server, Linux OS , external modem, Ethernet cables and analog phone line
Provides alert notification & remote service access for DS3000 and DS4000
  Works with your existing IBM Storage Manager client application to detect events
  Sends logs and status along with the alert to IBM for fast problem resolution
  Also allows IBM service to dial in to obtain additional information and logs to aid problem determination and speed problem resolution
Service coverage –
  All storage systems must be covered under IBM warranty or a current IBM maintenance contract
  The IBM support center will monitor alerts with the same coverage as that being provided for the storage server via the IBM hardware maintenance agreement, either:
    standard 9:00am-5:00pm, Monday-Friday, or
    extended 24 hours a day, 7 days a week
IBM provides the RSM for Storage software package as a no charge download
  RPQ and services contract SOW not required; no annual support fees
Notes: RSM for Storage is a software package that installs on customer supplied components to create a service gateway that provides alert notification and remote access for IBM Service.
It works with your existing IBM Storage Manager client application to detect critical events in your Ds3000 and DS4000 storage subsystems. When a problem is detected, log files from the affected subsystem are collected and sent along with the alert information to IBM Service for fast problem resolution
Also allows IBM service to dial in to the RSM system and from there access the affected storage subsystem to aid problem determination and speed problem resolution
All storage subsystems must be covered under IBM warranty or a current IBM maintenance contract. The IBM support center will respond with the with the same coverage as that being provided for the storage subsystem via your hardware maintenance agreement, either:
    standard 9:00am-5:00pm, Monday-Friday, or
    extended 24 hours a day, 7 days a week
IBM provides RSM for Storage software as a no charge download. Unlike similar solutions that were previously available, RSM for Storage does not require an RPQ or services contract SOW; and there are no annual support fees

## Slide 5: RSM for Storage – Planning and Installation Overview
Planning
  A comprehensive Planning, Installation and User’s Guide is available
  RSM for Storage can support up to 50 storage systems
    We recommend however that systems supported by an RSM for Storage system be in the same country.
Preparation
  Analog phone line
  Complete worksheets in Planning, Installation and User’s Guide
  IP connectivity from RSM system to:
    Storage Manager client, storage controllers, SMTP server, and the Internet
  Setup Server - Interface connections and latest firmware is installed
  Check to see if OS service pack images need to be downloaded before starting the installation
Installation
  RSM is designed for Customer Setup; the installation guide provides step by step instructions for
    Configuration of System x servers recommended for use with RSM for Storage
    Installation and configuration of the Linux OS
    Installation and configuration of the RSM for Storage software
  RSM Configuration
    Use prepared worksheets to configure RSM
    Set RSM system as destination for SNMP traps from Storage Manager
    Run the Configuration Test
  Activation - Contact IBM DASD support
Notes:   A comprehensive Planning, Installation and User’s Guide is available
  We recommend that the planning chapter be reviewed prior to deciding about suitability for your environment and before ordering hardware
Preparation
  Analog phone line
  Complete worksheets in Planning, Installation and User’s Guide
  IP connectivity -
  from RSM system to Storage Manger client, storage controllers, SMTP server
  Hardware
    Load latest server firmware (BIOS, Systems Management, …)
    Connect Ethernet, modem serial and phone line
  Check to see if service pack CD images need to be downloaded before starting the installation
Installation
  Software
    Linux OS installation – Detailed instructions are provided in the RSM documentation
    RSM software - one CD to load
  RSM Configuration
    Use worksheets to configure RSM
      Contact information
      Storage hostnames and IP addresses
      Modem phone number, SMTP server location
    Set RSM system as destination for SNMP traps from Storage Manager
    Run Configuration Test to validate information and connections
  Activation
    Contact IBM DASD support
      Will dial into RSM system and verify remote connection and alert path back to IBM
      Will complete installation by entering activation code

## Slide 6: RSM for Storage - Connections
RSM for Storage uses an Ethernet connection for problem reporting via email, and a modem for remote access by IBM Service
Customer notifications of events and remote access are also sent via email.
All storage systems, the management station (running IBM Storage Manager), your email server and Internet gateway must be accessible from the RSM for Storage server without requiring authorization through a firewall
Note: IBM Storage Manager is the application normally used for configuration and management of DS3000 and DS4000 subsystems and will usually already be installed. Security features of the RSM for Storage software require that it be installed on a dedicated server separate from the management station running IBM Storage Manager.
Notes: This diagram illustrates two possible LAN topologies
The blue LAN is your main campus LAN that provides access to the Internet.
Some companies also have their storage subsystems connected to this LAN.
The green segment shows storage subsystems connected to a separate “storage management” LAN.
The management station running IBM Storage Manager just be able to poll all storage subsystems in order to detect errors and may require two Ethernet connections.
The RSM for Storage system also needs access the storage subsystems, but also requires outbound access to the Internet.
When Storage Manager detects a problem, it is configured to send an SNMP trap to RSM. RSM then requests log files directly from the failed subsystem. These log files are then attached to an alert email and sent to IBM Service.
The next few charts will address some of the security features and explain why the system running the RSM software must be considered to be an dedicated Service Gateway and can not be combined on the management station.

## Slide 7: RSM for Storage – Security: Remote Access
RSM
Modem
Remote Access Security
Modem –
  The modem will not answer unless:
    One of the storage subsystems has an active alert
    or
    Remote Access has manually been enabled.
  RSM for Storage’s modem interface provides a console login interface for remote IBM Service users. No IP traffic is supported on this interface
Login –
  The service login password is changed at midnight UTC.
  Following a successful login, a response to a challenge string is required. Access to an internal IBM system is required for the login password and challenge response.
Notes: Starting with Remote Access to the system, there is no need for the modem to be allowed to answer an incoming call unless one of the storage subsystems is having a problem or unless you decide to manually enable remote access.
When the modem does answer, the connection only allow a console (or TTY) session. No IP traffic is allowed.
IBM Service uses a pre-defined remote service user-id (rservice) to log into the system, but the Linux password for all RSM systems is changed at mid-night UTC. A program that only runs on internal IBM systems must be used to determine the password.
Following a correct login, the user is next presented with a random challenge string. Again access to an internal IBM tool is required to determine the correct response. The response also includes the IBM User ID of the person that used the tool and is logged by the RSM system.

## Slide 8: RSM for Storage – Security: Internal Firewall
RSM for Storage includes an internal firewall to limit the scope of access a remote user has to your network.
To maintain the integrity if the firewall and other security controls, IBM users cannot change any security related configuration settings.
Internal Firewall
Inbound SNMP traps from management station. Outbound access to email server and IBM’s Web and FTP sites.
Access to Storage subsystems when they have active alerts
Customer enabled access subsystems or other configured SAN devices
Notes: Remote user have limited privileges and can not change any of the security settings of the system. A side effect of this is that they also can not update software or change configurations on the system.
Without an internal firewall, the remote user would have the same unlimited access to your network as a person sitting at the system. The RSM software configures an internal firewall on the RSM system to limit the access that users of the RSM system have to your network.
When no alerts are active, the firewall allows incoming SNMP traps and outbound SMTP email. (Yellow paths)
When an alert occurs, a rule is automatically added to the firewall to allow access to the configured controllers for the storage subsystem reporting the problem (Green paths)
There may be times when you want to allow IBM Service to be able to access a device to troubleshoot a problem (such as a performance issue) for a subsystem that is not reporting a failure. You can manually enable “service access” for any configured storage subsystem or even SAN switches. ( Blue paths)

## Slide 9: RSM for Storage – Security: Side Effects
Internal Firewall
  The internal firewall that limits the scope of what remote users can access on your network also limits access by applications running on the server.
  Management software such as IBM Storage Manager and IBM Director are also affected.
  Therefore RSM for Storage should be considered to be a single purpose appliance dedicated to problem reporting and remote access for IBM Service.
Notes: While the internal firewall effectively limits the scope of access for remote users, at the same time it also limits the access of any program running on the server.
Because management applications such as IBM Storage Manager or IBM Director require access to all devices being managed, the presence of this internal firewall prevents the use of the RSM server as a management station.
Therefore the RSM for Storage system should be considered to be a single purpose appliance dedicated to problem reporting and remote access for IBM Service.

## Slide 10: RSM for Storage – Security: Storage Subsystems
Storage Subsystem Security
  Storage Manager - Has the ability to require an administrative password in order to make changes to the systems configuration. It is recommended that this password be configured
  Controller shell environment - The controller shell environment is accessible using an remote login client at the controller’s Ethernet and serial ports when running PPP. Starting with Storage Manager version 8.4, the remote login server in the controller can be disabled. It is recommended that this be enabled only when required for remote service
  If access to either of these interfaces are required to resolve a problem, IBM Service will contact you.
RSM
Notes: While the RSM’s internal firewall can control IP access to a subsystem, there are other protections that are available.
IBM Storage Manager allows you to configure an Administration Password for each storage subsystem. Remote users that do not have this password can view subsystem configuration and download log files, but can not change the subsystem’s configuration.
The subsystem’s controllers also have a powerful, low level shell interface that is accessed using the rlogin protocol. The password for this interface is well known and can not be changed, and you should use the command in the IBM Storage Manager client to disable the remote login interface for your controllers. Access to the controller shell is usually only required to resolve very complex problems.

## Slide 11: RSM for Storage – Security: Customer Options
Customer Options
Automatic enable of remote access
Normally remote access (via modem) is enabled automatically when an alert is sent to IBM. You can choose to wait for IBM Service to contact you when an Alert is received and manually enable remote access at that time.
A Remote Access timeout
is configurable from 12 to 96 hours. You can manually disable remote access when service is complete or allow it to timeout thereby guaranteeing the system will return to a secure state without intervention.
Internet
Firewall
E-mail server
Modem
RSM
Internal Firewall
Required to limit remote access to specified systems
Switch
Host
Switch
Host
Mgmt Station
Other SAN devices can be configured to allow them to be accessed by a remote user
Notes: You do have several security related options that can be configured.
When a subsystem reports a problem you can choose to have RSM automatically enable remote access, or to wait to be called by IBM Service and then enable remote access manually.
Remote access will stay enabled until you manually disable it or the Remote Access timeout occurs. You can set this timeout from 12 to 96 hours.

## Slide 12: RSM for Storage – Knowing What Is Going On
Email Notifications
  Primary Contact - receives all notifications about RSM system operation and problems.
  Additional contacts can be configured for subsystems located at other sites. They only receive notifications related to subsystem problems.
Notification | Primary contact | Subsystem contacts
Remote Access is enabled or disabled | X | 
Remote User logs into the RSM for Storage system or logs out | X | 
Firewall is enabled or disabled | X | 
Remote Access is about to expire or has expired | X | X
An alert occurs for a subsystem | X | X
Daily status updates at local noon. | X | 
Daily status updates when a subsystem has an active alert | X | X
Daily phone line check fails | X | 
Notes: Email Notifications
Up to 20 contact people can be configured. One will be the primary contact for RSM related events and will receive all notifications about RSM system operation and problems.
As you may have subsystems located at several different sites, additional contacts can be configured and associated with those locations. These contacts will only receive notifications related to subsystem problems.
The planning, installation and users guide has more information about each of these notification emails.

## Slide 13: RSM for Storage – Required Elements
Hardware
  System x Server
    Can be ordered from IBM or an existing asset can be utilized, but it must be a dedicated server for RSM.
    System x server specifications are included in the Planning, Installation and User’s Guide
    The Compatibility Guide contains a list of System x servers that have been tested with RSM for Storage. RSM for Storage documentation includes specific configuration instructions for these servers.
  External Modem
    Any external modem meeting the requirements specified in the RSM for Storage Planning, Installation and User’s guide can be used.
    RSM for Storage has been tested with (and includes automatic configuration for) some modems. Refer to the Compatibility Guide for more information.
Software
  Linux Operating System
    RSM for Storage software has been tested with and is only supported on:
      SUSE Linux Enterprise Server, version 10
      SUSE Linux Enterprise Server, version 9, service pack 3
      Red Hat Enterprise Linux Advanced Server, version 4, update 4
    Refer to the Compatibility Guide for the latest information about newer versions of these Linux operating systems that may be supported for RSM for Storage.
  RSM for Storage works with your existing IBM Storage Manager application
    It is recommended that you should use the latest available versions of the IBM Storage Manager client and firmware for your storage subsystems.
  RSM for Storage Software
    The software package can be downloaded at no charge from:
    www.ibm.com/systems/storage/disk/rsm
Notes: The RSM for Storage service gateway has five elements:
System x server, an external modem, Linux operating system and RSM for Storage software which works with your exiting IBM Storage Manager application.
Any System x Server meeting the specifications listed in the Planning, Installation and User’s Guide can be used. However, the Compatibility Guide contains a list of System x servers that have been tested with RSM for Storage and the RSM for Storage documentation includes specific setup and configuration instructions for these servers.
Any external modem meeting the requirements specified in the RSM for Storage Planning, Installation and User’s guide can be used. The Compatibility Guide has a list of modems that RSM for Storage has been tested with. Some of these modems will be automatically configured by the RSM for Storage software for the country of installation.
RSM for Storage software is designed to run on Linux and has been tested with and only supported on:
-- SUSE Linux Enterprise Server, version 9, service pack 3
-- Red Hat Enterprise Linux Advanced Server, version 4, update 4
Before purchasing or installing the operating system, check the Compatibility Guide to see if support for a newer version has been announced.
RSM for Storage works with your existing IBM Storage Manager application which is configured to send SNMP traps to the RSM for Storage system.
RSM for Storage Software is distributed as an ISO image and is available as a free download from: www.ibm.com/systems/storage/disk/rsm

## Slide 14: RSM for Storage - Ordering Considerations
Server
  Ethernet LAN connections
    For installations where the storage management LAN is isolated from the LAN that provided external email connectivity, a server with two Ethernet ports is required.
    The recommended server, the x3250, has dual Ethernet ports to meet this requirement..
  Server HDD
    Note that hard disk drives for the server must be ordered as an option. HDDs are not part of the standard configuration
      Usually a single 80 GB SATA drive is appropriate.
      For higher availability, on-board RAID 1 (mirroring) using two drives can be configured. Check with System x sales and documentation for ordering and setup. Configuration of server RAID functions are part of the server BIOS and problem resolution and other assistance must be provided by System x support.
  Keyboard and Monitor
    For rack installations, often a KVM switch is available for connecting to the server. Ensure that keyboard, mouse and monitor are available.
Linux Operating System
  SLES is available from Novell at http://www.novell.com/products/server/
  RHEL AS is available from Red Hat at http://www.redhat.com/rhel/compare/server/
  If ordering a new System x server, the Linux OS may be available to be ordered as an “in the box” option.
Notes: A few considerations when selecting the required elements …
The servers recommended in the Compatibility Guide have dual Ethernet ports for situations where your storage and email/Internet are not accessible from a single connection. If using another server, you may need to add an Ethernet adapter for this situation.
If ordering a new System x server be aware that hard disk drives are not automatically with the various models and must be ordered as an option.
You can use a single 80 GB SATA drive, or for higher availability, use two drives with servers that have RAID 1support build into their system boards. Configuration of server RAID functions are part of the server BIOS and problem resolution and other assistance is provided by System x support.
Allow for keyboard, mouse and monitor connections to the system
If ordering a new System x server, the Linux OS may be available to be ordered as an “in the box” option. If using and existing server, you can order the operating system from Novell or Red Hat. Again check the Compatibility Guide for the latest information about supported versions of the Linux OS.

## Slide 15: RSM for Storage – More Information
Planning Questions
  Please review all RSM for Storage documentation available at:
    http://www.ibm.com/storage/disk/rsm
Additional technical questions:
  IBM Storage ATS Group
  or Don Newson newson@us.ibm.com
  or Bruce Allworth allworth@us.ibm.com
Notes: Review Chart..
Note to presenter:
Following the “Thank You” is an additional chart that discusses migration from two previous call home solutions:
IBM Alert Manager or IBM Service Alert.
Also included are two additional charts that provide specific ordering information for sales.

## Slide 16
Thank You!
Please visit ibm.com/storage for more information.
Notes: Thank you

## Slide 17: RSM for Storage – Migration
RSM for Storage:
  Replaces DS4000 Alert Manager which is no longer available
    Faster response time to alerts - first line of support is direct to IBM instead of managing through Engenio
    Improved security gives customer control of the remote access interface and new notifications when remote users connect to RSM and when any changes are made that affect security of the system.
    Lower cost – manages up to 50 storage subsystems per implementation Requires only an Ethernet connection. (No serial cables are required).
    RPQ and services contract SOW not required; no annual support fees
    IBM will continue to support existing Alert Manager agreements for the duration of the support contract.
  Replaces DS4000 Service Alert (email), which is no longer available
    RSM for Storage costs are comparable to or less than new DS4000 Service Alert cost
    Support for existing Service Alert contracts will continue until March of 2010.

## Slide 18
Sales and ordering resources
Notes: Thank you

## Slide 19: IBM RSM for Storage – Sales and Ordering Information
Customers must provide the Server, Modem, and Linux OS
  The hardware specifications are included in the “RSM Planning, Installation and User’s Guide” posted on the DS4000 Sales Kit web site
  The RSM for Storage – Compatibility Guide contains the latest information about supported and tested System x servers, external modems, and Linux OS distributions and versions.
System x Server
  Recommended System x configuration files are provided in the RSM Package on the DS4000 Sales Kit.
    Download and import these files into your configuration.
    Different files are provided depending upon the configuration tool being used.
      For eConfig tools, download .cfr files
      For SSCT tool, download .tp3 files
    Configuration files are provided with and without and operating system. See the next chart for details.
  If unsure how to order, contact System x Techline for System x configurations
    http://w3-03.ibm.com/support/techline.html
External Modem
  Customers may use any modem that meets the requirements specified in the RSM for Storage - Compatibility Guide
  If ordering a new modem one of the modems listed in the RSM for Storage Compatibility guide is recommended.
    These modems may be purchased from the manufacture or a distributor.
Continues on next chart

## Slide 20: IBM RSM for Storage – Sales and Ordering Information - 2
Linux OS
  Ordering the OS from IBM
    If ordering a new System x server, the Linux OS can be ordered as an “in the box” option. One of the recommended configuration files referenced on the previous chart includes the SLES operating system.
    Note that Red Hat RHEL AS is significantly more expensive and the provided configuration files only specify the SLES operating system.
    Customers that have a preference for Red Hat may already have a site license and therefore only need to order the server without any operating system.
  Ordering from the vendor
    SLES 10 is available from Novell at www.novell.com/products/server/
    RHEL 4 AS is available from Red Hat at www.redhat.com/rhel/compare/server
RSM Software:
  The code can be downloaded at no charge from: www.ibm.com/storage/disk/rsm
Installation:
  RSM is designed for Customer Setup
  Customers follow the instructions in the Planning, Installation and User’s Guide
  IBM Business Partners can provide services to simplify installation for customers

## Slide 21: RSM for Storage – Notices and Disclaimers
  Copyright © 2007 by International Business Machines Corporation. All rights reserved.
  No part of this document may be reproduced or transmitted in any form without written permission from IBM Corporation.
  Product data has been reviewed for accuracy as of the date of initial publication. Product data is subject to change without notice. This document could include technical inaccuracies or typographical errors. IBM may make improvements and/or changes in the product(s) and/or program(s) described herein at any time without notice. Any statements regarding IBM's future direction and intent are subject to change or withdrawal without notice, and represent goals and objectives only. References in this document to IBM products, programs, or services does not imply that IBM intends to make such products, programs or services available in all countries in which IBM operates or does business. Any reference to an IBM Program Product in this document is not intended to state or imply that only that program product may be used. Any functionally equivalent program, that does not infringe IBM's intellectually property rights, may be used instead.
  THE INFORMATION PROVIDED IN THIS DOCUMENT IS DISTRIBUTED "AS IS" WITHOUT ANY WARRANTY, EITHER EXPRESS OR IMPLIED. IBM EXPRESSLY DISCLAIMS ANY WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE OR NONINFRINGEMENT. IBM shall have no responsibility to update this information. IBM products are warranted, if at all, according to the terms and conditions of the agreements (e.g., IBM Customer Agreement, Statement of Limited Warranty, International Program License Agreement, etc.) under which they are provided. Information concerning non-IBM products was obtained from the suppliers of those products, their published announcements or other publicly available sources. IBM has not tested those products in connection with this publication and cannot confirm the accuracy of performance, compatibility or any other claims related to non-IBM products. IBM makes no representations or warranties, expressed or implied, regarding non-IBM products and services.
  The provision of the information contained herein is not intended to, and does not, grant any right or license under any IBM patents or copyrights. Inquiries regarding patent or copyright licenses should be made, in writing, to:
  IBM Director of Licensing
  IBM Corporation
  North Castle Drive
  Armonk, NY 10504-1785
  U.S.A.