ODI FOR FDDI, VERSION 1.0   JUNE 26, 1992
  _________________________________________





    About This File  . . . . . . . . . . . . . . . . . . . . . . . . . . . .  2
    Supported Platforms  . . . . . . . . . . . . . . . . . . . . . . . . . .  2
    IBMFDDIO LAN Driver Installation Procedure   . . . . . . . . . . . . . .  3
      DOS Workstation  . . . . . . . . . . . . . . . . . . . . . . . . . . .  3
      OS/2 Workstation   . . . . . . . . . . . . . . . . . . . . . . . . . .  4
      NetWare Server   . . . . . . . . . . . . . . . . . . . . . . . . . . .  5
    Configurable IBMFDDIO LAN Driver Parameters  . . . . . . . . . . . . . .  7
    Sample NET.CFG Configuration File for DOS and OS/2 Workstations  . . .   10
    Sample IBMFDDIO.CFG Configuration File for NetWare Server  . . . . . .   11
    IBMFDDIO LAN Driver Performance Tuning   . . . . . . . . . . . . . . .   12
      DOS Workstation  . . . . . . . . . . . . . . . . . . . . . . . . . .   12
      OS/2 Workstation   . . . . . . . . . . . . . . . . . . . . . . . . .   12
      NetWare Server   . . . . . . . . . . . . . . . . . . . . . . . . . .   12
    IBM FDDI Adapter Custom Statistic Counters   . . . . . . . . . . . . .   13
    Messages for the IBMFDDIO LAN Driver   . . . . . . . . . . . . . . . .   16



































  (C) Copyright IBM Corp. 1992                                                1




  ABOUT THIS FILE

  This file describes the use of the IBMFDDIO LAN drivers with IBM FDDI
  Adapters.  These LAN drivers support the IBM FDDI Adapter in the Novell
  Netware environment.

  This file is an extension of the IBM FDDI FIBER BASE ADAPTER/A INSTALLATION
  AND TESTING INSTRUCTIONS or the IBM FDDI COPPER BASE ADAPTER/A INSTALLATION
  AND TESTING INSTRUCTIONS that is shipped with the adapter.  This file
  describes the installation and configuration of the IBM FDDI Open Datalink
  Interface (ODI) (IBMFDDIO) LAN drivers.  It contains information about the
  following topics:

  o   Supported platforms

  o   Software installation procedures

  o   Configurable IBMFDDIO LAN driver parameters

  o   Performance tuning the IBMFDDIO LAN drivers

  o   IBM FDDI Adapter Custom Statistic Counters

  o   Messages for the IBMFDDIO LAN driver.


  SUPPORTED PLATFORMS

  The IBMFDDIO LAN driver is supported in any of the hardware environments
  supported by the IBM FDDI Adapter.  See the IBM FDDI FIBER BASE ADAPTER/A
  INSTALLATION AND TESTING INSTRUCTIONS or the IBM FDDI COPPER BASE ADAPTER/A
  INSTALLATION AND TESTING INSTRUCTIONS for information about supported
  hardware.

  The following operating system environments are supported:

  o   Novell NetWare 3.11

  o   IBM DOS 3.3

  o   IBM DOS 4.0

  o   IBM DOS 5.0

  o   IBM OS/2 1.3

  o   IBM OS/2 2.0.









                                   ODI for FDDI, Version 1.0   June 26, 1992  2






  IBMFDDIO LAN DRIVER INSTALLATION PROCEDURE

  This section describes how to install the IBMFDDIO LAN driver on each of the
  supported platforms (DOS, OS/2, or NetWare Server).

  See the IBM FDDI FIBER BASE ADAPTER/A INSTALLATION AND TESTING INSTRUCTIONS
  or the IBM FDDI COPPER BASE ADAPTER/A INSTALLATION AND TESTING INSTRUCTIONS
  that is shipped with the adapter for instructions on how to install the IBM
  FDDI Adapter.


  DOS Workstation

  This section describes how to install the IBMFDDIO LAN driver on a DOS
  workstation.

  To install the IBMFDDIO LAN driver on a DOS workstation, perform the
  following steps:

  1.  Choose a target directory path on the diskette or the fixed disk (for
      example, C:\NETWARE) for installation of the IBMFDDIO LAN driver and its
      associated files.  All files (in step 2 and step 3, below) should be
      copied to this target directory.

  2.  Copy the following files to the target directory:

      o   IBMFDDIO.COM

  3.  Copy IBMFDDI.BIN from the root directory of the IBM FDDI Adapter Option
      Diskette to the target directory.

      NOTE:  The IBMFDDI.BIN file MUST be in the same directory as the
      IBMFDDIO.COM file.

  4.  Add the directory path from step 1 to the PATH= statement in the
      AUTOEXEC.BAT file.  For example:

         PATH=C:\DOS;C:\NETWARE;

  5.  Add the following lines to the AUTOEXEC.BAT file (after the PATH=
      statement):

         LSL
         IBMFDDIO
         IPXODI
         NETX
         REM  Add ROUTE.COM only if Source Routing is needed.
         ROUTE

      NOTE:  See NOVELL NETWARE ODI SHELL FOR DOS for information about
      ROUTE.COM.

  6.  If you need to change any IBMFDDIO LAN driver parameter values from
      defaults, edit the NET.CFG file to change only those parameters.  See


                                   ODI for FDDI, Version 1.0   June 26, 1992  3






      "Sample NET.CFG Configuration File for DOS and OS/2 Workstations" for a
      sample NET.CFG file.

  You can use any DOS text editor to edit AUTOEXEC.BAT and NET.CFG.  See NOVELL
  NETWARE ODI SHELL FOR DOS for more information about AUTOEXEC.BAT and
  NET.CFG.


  OS/2 Workstation

  This section describes how to install the IBMFDDIO LAN driver on an OS/2
  workstation.

  To install the IBMFDDIO LAN driver on an OS/2 workstation perform the
  following steps:

  1.  Choose a target directory path on the diskette or the fixed disk (for
      example, C:\NETWARE) for installation of the IBMFDDIO LAN driver and its
      associated files.  All files (in step 2 and step 3, below) should be
      copied to this target directory.

  2.  Copy the following files to the target directory:

      o   IBMFDDIO.OS2

  3.  Copy IBMFDDI.BIN from the root directory of the IBM FDDI Adapter Option
      Diskette to the target directory.

      NOTE:  The IBMFDDI.BIN file MUST be in the same directory as the
      IBMFDDIO.OS2 file.

  4.  Add the following lines to the CONFIG.SYS file (if not already present):

         DEVICE=C:\NETWARE\LSL.SYS
         RUN=C:\NETWARE\DDAEMON.EXE
         DEVICE=C:\NETWARE\IBMFDDIO.OS2

         REM Add ROUTE.SYS only if Source Routing is needed.
         DEVICE=C:\NETWARE\ROUTE.SYS

         DEVICE=C:\NETWARE\IPX.SYS

      NOTES:

      a.  The Novell NetWare OS/2 support files must be installed before
          running the OS/2 requester.  See NOVELL NETWARE REQUESTER FOR OS/2
          for more information.

      b.  See NOVELL NETWARE REQUESTER FOR OS/2 for information about
          ROUTE.SYS.

      c.  These lines must appear in the order indicated.




                                   ODI for FDDI, Version 1.0   June 26, 1992  4






      See NOVELL NETWARE REQUESTER FOR OS/2 for information about how to edit
      the CONFIG.SYS file.

  5.  If you need to change any IBMFDDIO LAN driver parameter values from their
      defaults, edit the NET.CFG file to change only those parameters.  You can
      use any text editor to edit the NET.CFG file.  See "Sample NET.CFG
      Configuration File for DOS and OS/2 Workstations" for a sample NET.CFG
      file.

  See NOVELL NETWARE REQUESTER FOR OS/2 for more information about CONFIG.SYS
  and NET.CFG.


  NetWare Server

  This section describes how to install the IBMFDDIO LAN driver on a NetWare
  Server.

  To install the IBMFDDIO LAN driver on a NetWare Server, perform the following
  steps:

  1.  Choose a target directory path on the diskette or the fixed disk (for
      example, C:\NW) for installation of the IBMFDDIO LAN driver and its
      associated files.  All files (in step 2, below) should be copied to this
      target directory.

  2.  Copy the following files to the target directory:

      o   IBMFDDIO.LAN

      o   MSM.NLM (MSM311.NLM if running Novell NetWare 3.11)

      o   FDDITSM.NLM.

  3.  Add the following lines to the STARTUP.NCF file:

        Set Minimum Packet Receive Buffers = 30
        Set Maximum Physical Receive Packet Size = 4500

        NOTE:  If running on NetWare 3.11,
        Set Maximum Physical Receive Packet Size = 4202

  4.  Add the following line to the AUTOEXEC.NCF file:

        LOAD C:\NW\IBMFDDIO.LAN @IBMFDDIO.CFG

      NOTES:

      a.  @IBMFDDDIO.CFG is an optional command line parameter (see step 5,
          below).

      b.  IBMFDDIO.LAN automatically loads MSM.NLM (MSM311.NLM if running
          Novell NetWare 3.11) and FDDITSM.NLM.



                                   ODI for FDDI, Version 1.0   June 26, 1992  5






      See NOVELL NETWARE SYSTEM ADMINISTRATION for more information about the
      AUTOEXEC.NCF and STARTUP.NCF files.

  5.  If you need to change any IBMFDDIO LAN driver parameter values from their
      defaults, these parameters can be specified on the command line when the
      IBMFDDIO LAN driver is loaded or they can be specified by creating an
      IBMFDDIO.CFG configuration file.  If the optional @IBMFDDIO.CFG command
      line parameter is used to specify an IBMFDDIO.CFG configuration file,
      then the configuration file must be located in the same directory as the
      IBMFDDIO.LAN file.  You can use any text editor to create or edit the
      IBMFDDIO.CFG file.  See "Sample IBMFDDIO.CFG Configuration File for
      NetWare Server" for a sample IBMFDDIO.CFG file.

  6.  If you run the MONITOR.NLM program at your NetWare server, obtain the
      latest copy of the MONITOR.NLM program from Novell.  Update your NetWare
      servers with the latest copy of the MONITOR.NLM program.








































                                   ODI for FDDI, Version 1.0   June 26, 1992  6






  CONFIGURABLE IBMFDDIO LAN DRIVER PARAMETERS

  The following parameters can be configured at DOS and OS/2 workstations by
  setting keywords in the NET.CFG file.  These parameters can be configured at
  the NetWare Server by setting keywords on the command line and in the
  IBMFDDIO.CFG file.  A sample NET.CFG file is shown in "Sample NET.CFG
  Configuration File for DOS and OS/2 Workstations." A sample IBMFDDIO.CFG file
  is shown in "Sample IBMFDDIO.CFG Configuration File for NetWare Server."

  SLOT
         This keyword defines the slot number of the corresponding IBM FDDI
         Adapter in the workstation.  The system defaults to the lowest
         numbered slot containing a network adapter of this type.  Specify this
         keyword when more than one IBM FDDI Adapter is present in the same
         workstation.  This keyword must be within the range 1-8.

  FRAME
         This keyword defines the frame type used with the network adapter.
         The default is FDDI_802.2.  The value for this keyword must be one of
         the following:

         o   FDDI_802.2

         o   FDDI_SNAP

  NODE ADDRESS (OS/2 or DOS) or NODE (Server)
         To set a locally administered address for the adapter, type in the
         local address you want to use.  The local address must contain 12
         hexadecimal characters and can be specified in either MSB (Most
         Significant Bit) or LSB (Least Significant Bit --the default) format.
         To specify a MSB node address the letter "M" immediately follows the
         last digit of the node address.  To specify a LSB node address the
         letter "L" immediately follows the last digit of the node address.
         Since LSB is the default format for the node address parameter, the
         use of a letter "L" at the end of a node address is for clarity.

         This keyword is specified as NODE ADDRESS in NET.CFG for DOS and OS/2
         workstations.  See "Sample NET.CFG Configuration File for DOS and OS/2
         Workstations" for a sample NET.CFG file.  This keyword is specified on
         the command line or in the IBMFDDIO.CFG as NODE for the NetWare
         Server.  See "Sample IBMFDDIO.CFG Configuration File for NetWare
         Server" for a sample IBMFDDIO.CFG file.

         If a node address is specified in MSB format, the characters must be
         within the range 400000000000-7FFFFFFFFFFF.  To specify a node address
         in MSB format, append an "M" to the end of the address (for example,
         400000000001M).  This address specified in LSB format would be
         020000000080L.








                                   ODI for FDDI, Version 1.0   June 26, 1992  7






         NOTES:

         1.  Do not assign the same local address to two or more stations.
             Severe station communication or network failures may occur when
             two or more stations are assigned the same address.

         2.  If you do not assign a locally administered address, the adapter
             uses the universally administered address permanently embedded on
             the adapter.

  ATTACHMENTCLASS
         This keyword defines the station as either a single attachment station
         or a dual attachment station.

             For single attachment, set ATTACHMENTCLASS to 1.
             For dual attachment, set ATTACHMENTCLASS to 2.

         If ATTACHMENTCLASS is not specified, it is set according to the
         adapters (base or base and extender) present in the system.

  PMFPASSWORD
         This keyword defines the password that all remote PMF (Parameter
         Management Frame) requests must provide to change FDDI attributes
         within this adapter.  The value for PMFPASSWORD must be 8 ASCII
         characters long and be enclosed in double quotes.  The PMFPASSWORD
         parameter is not case sensitive since lower case letters will be
         converted to upper case.

         The double quote character can be specified within the PMFPASSWORD by
         preceding the double quote character with a backslash (\) character
         (\").  Hexadecimal characters can be specified in the ASCII string
         with a "\" followed by one or two hexadecimal character digits.  To
         specify an ASCII "\" character, two backslashes (\\) must immediately
         follow each other.  Password protection can be disabled by setting
         this keyword to all zeros (default), or by not specifying a
         PMFPASSWORD.

  USERDATA
         This keyword defines a character string up to 32 characters long.  The
         character string must be enclosed in double quotes.  The USERDATA
         string cannot contain embedded double quotes and is not case sensitive
         since lower case letters will be converted to upper case.

  RXBUFFERS
         This keyword defines the number of receive buffers used by the
         IBMFDDIO LAN driver.  Values vary by workstation type as follows:

         DOS WORKSTATIONS

                   The value for this keyword must be: 1, 2, or 4; the default
                   is 2.  (Each receive buffer takes 4500 bytes of memory.)





                                   ODI for FDDI, Version 1.0   June 26, 1992  8






         OS/2 WORKSTATIONS

                   The value for this keyword must be: 1, 2, 4, or 8; the
                   default is 4.  (Receive buffer size is defined by the LSL
                   buffer configuration.  See NOVELL NETWARE REQUESTER FOR OS/2
                   for more information.)

         NETWARE SERVER

                   The value for this keyword must be: 1, 2, 4, 8, or 16; the
                   default is 16.  (Receive buffer size is defined by the
                   server SET command.  See NOVELL NETWARE SYSTEM
                   ADMINISTRATION for more information.)

  TXBUFFERS
         This keyword defines the number of 4500-byte transmit buffers used by
         the IBMFDDIO LAN driver.  This keyword is applicable only to DOS or
         OS/2 workstations; it is not available at the NetWare Server.  Values
         vary by workstation type as follows:

         DOS WORKSTATIONS

                   The value for this keyword must be: 1, 2, or 4; the default
                   is 2.

         OS/2 WORKSTATIONS

                   The value for this keyword must be: 1, 2, 4, or 8; the
                   default is 4.



























                                   ODI for FDDI, Version 1.0   June 26, 1992  9






  SAMPLE NET.CFG CONFIGURATION FILE FOR DOS AND OS/2 WORKSTATIONS

  Link Support
          ; For OS/2 workstations, specify the following BUFFERS
          ; parameter to receive maximum size FDDI frames of 4500.
          BUFFERS 10 4500
  Link Driver IBMFDDIO
          ; The following are sample ODI keywords for IBMFDDIO:
          NODE ADDRESS 400000000001M
          SLOT  2
          FRAME FDDI_802.2

          ; The following are ODI FDDI keywords with sample values:
          ATTACHMENTCLASS  1
          PMFPASSWORD      "12345678"
          USERDATA         "IBM FDDI Adapter at DOS WS 12345"
          ; Default RXBUFFERS is 2 for DOS, and 4 for OS/2.
          RXBUFFERS        2
          ; Default TXBUFFERS is 2 for DOS, and 4 for OS/2.
          TXBUFFERS        2




































                                  ODI for FDDI, Version 1.0   June 26, 1992  10






  SAMPLE IBMFDDIO.CFG CONFIGURATION FILE FOR NETWARE SERVER

     ; The following are the supported ODI keywords for IBMFDDIO:
     NODE=400000000002M
     SLOT=2
     FRAME=FDDI_802.2

     ; The following are ODI FDDI keywords with sample values:
     ATTACHMENTCLASS=1
     PMFPASSWORD="12345678"
     USERDATA="IBM FDDI Adapter at Server"
     RXBUFFERS=16












































                                  ODI for FDDI, Version 1.0   June 26, 1992  11






  IBMFDDIO LAN DRIVER PERFORMANCE TUNING

  This section describes how to get the best performance from the IBM FDDI
  Adapter and IBMFDDIO LAN drivers.  Since the maximum frame size that an IBM
  FDDI Adapter can send is 4500 bytes, the receive buffers used by the IBMFDDIO
  LAN drivers must be configured to 4500 bytes.  Below are the instructions on
  how to configure the IBMFDDIO LAN driver receive buffers to 4500 bytes on
  each of the platforms.


  DOS Workstation

  The size of the receive buffers used by the DOS IBMFDDIO.COM LAN driver is
  4500 bytes and is not configurable.  The number of receive buffers used by
  the DOS IBMFDDIO.COM LAN driver can be configured by specifying the RXBUFFERS
  keyword in the NET.CFG file.  While changing the number of receive buffers
  used by the IBMFDDIO.COM LAN driver may not change the performance of the IBM
  FDDI Adapter greatly, it will change the amount of DOS memory that is used by
  the IBMFDDIO.COM by 4500 per receive buffer.

  See "Sample NET.CFG Configuration File for DOS and OS/2 Workstations" for a
  sample NET.CFG file.


  OS/2 Workstation

  Since the IBMFDDIO.OS2 LAN driver uses Link Support Layer (LSL) buffers to
  receive frames, the size of receive buffers used by the IBMFDDIO.OS2 LAN
  driver is configurable by changing the size of the LSL buffers in the NET.CFG
  file.  Create or edit the NET.CFG file, and under the Link Support heading,
  change the second value of the BUFFERS parameter to 4500, and then restart
  your computer.

  See "Sample NET.CFG Configuration File for DOS and OS/2 Workstations" for a
  sample NET.CFG file.


  NetWare Server

  Since the IBMFDDIO.LAN driver uses NetWare receive buffers to receive frames,
  the size of receive buffers used by the IBMFDDIO.LAN driver is configurable
  by changing the size of the NetWare receive buffers.  Create or edit the
  STARTUP.NCF file and add the following line to change the size of the receive
  buffers:

    Set Maximum Physical Receive Packet Size = 4500

    NOTE:  If running on NetWare 3.11,
    Set Maximum Physical Receive Packet Size = 4202







                                  ODI for FDDI, Version 1.0   June 26, 1992  12






  IBM FDDI ADAPTER CUSTOM STATISTIC COUNTERS

  The custom statistic counters give the user information that is specific to
  the IBM FDDI Adapter and IBMFDDIO LAN drivers.  Following are descriptions of
  the custom statistic counters and what action, if any, should be taken based
  on these counters.


  Receive Frames Discarded

     Description:  This counter indicates the number of frames that were
                   received by the IBM FDDI Adapter but were discarded by
                   the adapter because they were not processed within the
                   allowed time period by the IBMFDDIO LAN driver.

    Cause/Action:  If this counter steadily increases, it may indicate
                   a problem at your computer.  Try increasing the number
                   of link support buffers for an OS/2 workstation, the
                   RXBUFFERS parameter in the NET.CFG file for a DOS work-
                   station, or the number of NetWare Server communications
                   buffers for a server; then, reload the IBMFDDIO LAN
                   driver.  If this problem persists, contact you network
                   administrator.

  Transmit Frames Discarded

     Description:  This counter indicates the number of frames that were not
                   transmitted by the IBM FDDI Adapter within the allowed
                   time period; the frames were discarded by the IBMFDDIO LAN
                   driver.

    Cause/Action:  Possible explanations for this problem are as follows:
                      1.  The FDDI ring is experiencing problems and,
                          therefore, the IBM FDDI Adapter could not transmit
                          frames.  If this problem persists, contact your
                          network administrator.

                      2.  The IBM FDDI Adapter is not responding.
                          Check the adapter by running the diagnostic tests
                          located on the Option Diskette that was shipped
                          with the IBM FDDI Adapter.  If there are no
                          problems with the adapter, reload the IBMFDDIO LAN
                          driver.


  Adapter Check Count

     Description:  This counter indicates the number of adapter check errors
                   reported by the IBM FDDI Adapter.

    Cause/Action:  The IBM FDDI Adapter and IBMFDDIO LAN driver
                   may recover from this error.

                   If this counter continues to increase, check the adapter


                                  ODI for FDDI, Version 1.0   June 26, 1992  13






                   by running the adapter diagnostic tests located on the
                   Option Diskette that was shipped with the IBM FDDI
                   Adapter.  If there are no problems with the adapter,
                   reload the IBMFDDIO LAN driver.


  Adapter Diagnostic Errors

     Description:  This counter indicates the number of diagnostic
                   test errors reported by the IBM FDDI Adapter.

    Cause/Action:  If this counter continues to increase, check the adapter
                   by running the adapter diagnostic tests located on the
                   Option Diskette that was shipped with the IBM FDDI
                   Adapter.  If there are no problems with the adapter,
                   reload the IBMFDDIO LAN driver.


  Disconnect Frames Received

     Description:  This counter indicates the number of disconnect
                   request frames that were received by the IBM
                   FDDI Adapter from another FDDI adapter.

    Cause/Action:  If you are experiencing problems communicating
                   on the network and this counter is nonzero,
                   reload the IBMFDDIO LAN driver.

                   If this counter continues to be nonzero, contact your
                   network administrator.


  Micro Channel Check Count

     Description:  This counter indicates that an error occurred with the
                   Micro Channel bus.

    Cause/Action:  The IBM FDDI Adapter detected an error with the
                   Micro Channel bus while accessing or attempting to
                   access the bus.

                   If this counter continues to increase, run the
                   diagnostics on the reference disk that came with your
                   computer to test for problems with the Micro Channel
                   bus.


  Microcode CRC Errors

     Description:  The cyclic redundancy check (CRC) of the IBM FDDI
                   Adapter microcode did not match the expected value.

    Cause/Action:  When the IBM FDDI Adapter is initialized or reset,
                   it performs a CRC of its microcode to make sure that the


                                  ODI for FDDI, Version 1.0   June 26, 1992  14






                   microcode has not become corrupted.  If this counter
                   is nonzero, perform one of the following actions:

                      For a Server:
                        Replace the IBMFDDIO LAN driver with a copy from the
                        original distribution diskette.

                      For a DOS or OS/2 workstation:
                        Replace the IBMFDDIO LAN driver with a copy from the
                        original distribution diskette.
                        Replace the IBMFDDI.BIN microcode file with a copy
                        from the IBM FDDI Adapter Option Diskette that was
                        shipped with your IBM FDDI Adapter.

                   If the counter continues to be nonzero, contact your
                   network administrator or IBM support center for a new
                   copy of the appropriate file.


  Path Test Errors

     Description:  This counter indicates that the IBM FDDI Adapter
                   detected an error while performing a path test
                   when inserting into the ring.

    Cause/Action:  When the IBM FDDI Adapter attempts to insert into
                   the ring, it performs a path test.  This test checks
                   the various data paths on the adapter to make sure that
                   the adapter is capable of sending and receiving data.

                   If this counter is nonzero, there may be a hardware
                   problem with the IBM FDDI Adapter. Check the adapter
                   by running the adapter diagnostic tests located on the
                   Option Diskette that was shipped with the IBM FDDI
                   Adapter.  If this problem persists, contact your network
                   administrator or IBM support center.


  Warm Start Count

     Description:  This counter indicates how many times the IBM FDDI
                   Adapter has restarted itself because of detected errors.

    Cause/Action:  The IBM FDDI Adapter will restart itself if it detects
                   an error that can be solved by restarting the adapter
                   microcode.  The IBM FDDI Adapter and IBMFDDIO LAN
                   driver may recover from this condition.

                   If you are experiencing problems with your network and
                   this counter continues to increase, check the adapter
                   by running the adapter diagnostic tests located on the
                   Option Diskette that was shipped with the IBM FDDI
                   Adapter.  If there are no problems with the adapter,
                   reload the IBMFDDIO LAN driver.


                                  ODI for FDDI, Version 1.0   June 26, 1992  15






  MESSAGES FOR THE IBMFDDIO LAN DRIVER

  IBMFDDIO-xx-yyy  Where the -xx- can be DOS, OS/2, or NW (NetWare Server).

  IBMFDDIO-xx-001: The LSL is not loaded.

           Cause:  The Link Support Layer (LSL) module was not loaded
                   before loading the IBMFDDIO LAN driver.  The LSL is
                   required by the IBMFDDIO LAN driver.
                   The IBMFDDIO LAN driver did not load.

           Action: Load the LSL module for the operating system you are
                   using.  Refer to the appropriate Novell NetWare manual
                   listed below for information about loading the LSL module
                   for your operating system.

                   For DOS:
                     NOVELL NETWARE ODI SHELL FOR DOS

                   For OS/2:
                     NOVELL NETWARE REQUESTER FOR OS/2


  IBMFDDIO-xx-002: The LSL has no room for a board using Frame <type>.

           Variable Data:  <type>
                      - FDDI_802.2
                      - FDDI_SNAP

           Cause:  An error occurred while trying to load the IBMFDDIO
                   LAN driver with the specified frame type.  The
                   maximum number of LAN drivers may already be loaded.
                   The IBMFDDIO LAN driver did not load.

           Action: Unload LAN drivers that are not being used, and then
                   load the IBMFDDIO LAN driver.  If this error persists,
                   load the IBMFDDIO LAN driver before loading other LAN
                   drivers.  This may require you to edit the CONFIG.SYS
                   or AUTOEXEC.BAT file before restarting your workstation.
                   Refer to the Novell NetWare manual listed below for
                   information about loading LAN drivers for your operating
                   system.

                   For DOS:
                     NOVELL NETWARE ODI SHELL FOR DOS

                   For OS/2:
                     NOVELL NETWARE REQUESTER FOR OS/2


  IBMFDDIO-xx-003: Could not find IBMFDDIO MLID to unload.

           Cause:  The IBMFDDIO LAN driver or Multiple Link Interface
                   Driver (MLID) could not be unloaded.  The IBMFDDIO


                                  ODI for FDDI, Version 1.0   June 26, 1992  16






                   LAN driver may not have been loaded or was previously
                   unloaded.

           Action: None.


  IBMFDDIO-xx-004: A TSR is loaded above the IBMFDDIO MLID.

           Cause:  The IBMFDDIO Multiple Link Interface Driver (MLID)
                   could not be unloaded because Terminate Stay Resident
                   (TSR) programs were loaded after the IBMFDDIO LAN driver
                   was loaded.

           Action: Try to unload the TSR programs that were loaded after
                   IBMFDDIO LAN driver, and then unload the IBMFDDIO LAN
                   driver.  If some TSR programs cannot be unloaded, then
                   load the IBMFDDIO LAN driver after loading the TSR
                   programs that could not be unloaded.  You may need to
                   edit the CONFIG.SYS or AUTOEXEC.BAT file to change the
                   order of loading the IBMFDDIO LAN driver.  Refer to the
                   Novell NetWare manual listed below for information
                   about loading LAN drivers for your operating system.

                   For DOS:
                     NOVELL NETWARE ODI SHELL FOR DOS

                   For OS/2:
                     NOVELL NETWARE REQUESTER FOR OS/2


  IBMFDDIO-xx-005: IBMFDDIO MLID could not unload; the operation is
                   aborted.

           Cause:  An error occurred while trying to unload the IBMFDDIO
                   Multiple Link Interface Driver (MLID).

           Action: Try to unload the IBMFDDIO LAN driver again.  If this
                   error persists, check the adapter by running the
                   adapter diagnostic tests located on the Option Diskette
                   that was shipped with the IBM FDDI Adapter.  If the
                   adapter passes the diagnostic tests and this error
                   continues to occur, contact your network administrator
                   or IBM support center.


  IBMFDDIO-xx-006: The adapter did not initialize.  IBMFDDIO did not load.

           Cause:  An error occurred during initialization of the IBM FDDI
                   Base Adapter/A and Extended Adapter/A.  The reason for
                   this error is in the message
                   that is written on the screen above this error message.
                   The IBMFDDIO LAN driver did not load.

           Action: Follow the recommended action in the message that is


                                  ODI for FDDI, Version 1.0   June 26, 1992  17






                   written on the screen above this error message.


  IBMFDDIO-xx-007: You need another MLID Section Heading in the NET.CFG file
                   in order to load the MLID again.

           Cause:  The IBMFDDIO LAN driver could not be loaded again because
                   there was no configuration information describing how
                   to load it.  The IBMFDDIO LAN driver can be loaded once
                   with default values.  If the IBMFDDIO LAN driver is loaded
                   again, configuration information for loading an additional
                   copy of the IBMFDDIO LAN driver must be provided in an MLID
                   Section Heading of the NET.CFG file.

           Action: Edit the NET.CFG file and add an MLID Section Heading
                   for the IBMFDDIO LAN driver.  Refer to the appropriate
                   Novell NetWare manual listed below for information
                   about editing a NET.CFG file, and to
                   "Configurable IBMFDDIO LAN Driver Parameters"
                   for information about valid NET.CFG file parameters for
                   the IBMFDDIO LAN driver.

                   For DOS:
                     NOVELL NETWARE ODI SHELL FOR DOS

                   For OS/2:
                     NOVELL NETWARE REQUESTER FOR OS/2


  IBMFDDIO-xx-008: A NET.CFG file is required to load the MLID again.

           Cause:  The IBMFDDIO LAN driver could not be loaded again
                   because there was no NET.CFG file describing how to
                   load it.  The IBMFDDIO LAN driver can be loaded once
                   with default values.  If the IBMFDDIO LAN driver is
                   loaded again, a NET.CFG file containing an MLID Section
                   Header for the IBMFDDIO LAN driver must be created.

           Action: Create a NET.CFG file and add an MLID Section Heading
                   for the IBMFDDIO LAN driver.  Refer to the appropriate
                   Novell NetWare manual listed below for information
                   about editing an NET.CFG file, and to
                   "Configurable IBMFDDIO LAN Driver Parameters"
                   for information about valid NET.CFG file parameters for
                   the IBMFDDIO LAN driver.

                   For DOS:
                     NOVELL NETWARE ODI SHELL FOR DOS

                   For OS/2:
                     NOVELL NETWARE REQUESTER FOR OS/2


  IBMFDDIO-xx-009: The NET.CFG entry has been ignored.


                                  ODI for FDDI, Version 1.0   June 26, 1992  18






           Cause:  An entry was specified in the NET.CFG file for the IBM
                   FDDI Adapter but was ignored. The entry may have been
                   incorrect or incompatible with the IBM FDDI hardware.
                   The IBMFDDIO LAN driver was loaded.

           Action: Refer to
                   "Configurable IBMFDDIO LAN Driver Parameters"
                   for information about valid NET.CFG file parameters for
                   the IBMFDDIO LAN driver.


  IBMFDDIO-xx-010: The IBMFDDIO MLID has been successfully removed.

           Cause:  The IBMFDDIO LAN driver or Multiple Link Interface
                   Driver (MLID) was unloaded successfully.

           Action: None.


  IBMFDDIO-xx-011: The MLID does not support frame <type>.
                   The protocol keyword has been ignored.

           Variable Data:   <type>
                     - Supplied from the NET.CFG file, the frame
                       type field of the PROTOCOL keyword found in the
                       MLID Section Heading for the IBMFDDIO LAN driver.

           Cause:  The frame type field of the PROTOCOL keyword that
                   was found in the IBMFDDIO MLID Section Heading of the
                   NET.CFG file is not supported by the IBMFDDIO LAN driver.

           Action: Edit the NET.CFG file and specify a valid frame type
                   parameter for the PROTOCOL keyword in the MLID Section
                   Heading for the IBMFDDIO LAN driver.  Refer to the
                   appropriate Novell NetWare manual listed below for
                   information about editing a NET.CFG file, and to
                   "Configurable IBMFDDIO LAN Driver Parameters"
                   for information about valid NET.CFG file parameters for
                   the IBMFDDIO LAN driver.

                   For DOS:
                     NOVELL NETWARE ODI SHELL FOR DOS

                   For OS/2:
                     NOVELL NETWARE REQUESTER FOR OS/2


  IBMFDDIO-xx-012: The protocol keyword must have a frame type.  Entry ignored.

           Cause:  The PROTOCOL keyword that was found in the IBMFDDIO
                   MLID Section Heading of the NET.CFG file did not
                   specify a required frame type parameter.



                                  ODI for FDDI, Version 1.0   June 26, 1992  19






           Action: Edit the NET.CFG file and add a valid frame type
                   parameter to the PROTOCOL keyword in the MLID Section
                   Heading for the IBMFDDIO LAN driver.  Refer to the
                   appropriate Novell NetWare manual listed below for
                   information about editing a NET.CFG file, and to
                   "Configurable IBMFDDIO LAN Driver Parameters"
                   for information about valid NET.CFG file parameters for
                   the IBMFDDIO LAN driver.

                   For DOS:
                     NOVELL NETWARE ODI SHELL FOR DOS

                   For OS/2:
                     NOVELL NETWARE REQUESTER FOR OS/2


  IBMFDDIO-xx-013: The MLID could not register Protocol ID <number>
                   for protocol stack <name> for frame type <frame>.

           Variable Data:  <number> -  Hexadecimal protocol ID for
                                       PROTOCOL keyword
                           <name>   -  Name parameter for PROTOCOL
                                       keyword
                           <frame>  -  Frame type parameter for
                                       PROTOCOL keyword.

           Cause:  One or more of the parameters specified for the PROTOCOL
                   keyword in the NET.CFG file for the IBMFDDIO LAN driver
                   was incorrect.

           Action: Edit the NET.CFG file and correct the incorrect PROTOCOL
                   keyword parameters in the MLID Section Heading for the
                   IBMFDDIO LAN driver.  Refer to the appropriate Novell
                   NetWare manual listed below for information about editing
                   a NET.CFG file, and to
                   "Configurable IBMFDDIO LAN Driver Parameters"
                   for information about valid NET.CFG file parameters for
                   the IBMFDDIO LAN driver.

                   For DOS:
                     NOVELL NETWARE ODI SHELL FOR DOS

                   For OS/2:
                     NOVELL NETWARE REQUESTER FOR OS/2


  IBMFDDIO-xx-014: This version of the LSL is not supported.

           Cause:  The version level of the LSL module that is loaded is no
                   longer supported.  The IBMFDDIO LAN driver did not load.

           Action: Unload the LSL module and load a later version of the LSL
                   module.



                                  ODI for FDDI, Version 1.0   June 26, 1992  20






  IBMFDDIO-xx-015: The frame type is already active for the frame <type>.

           Variable Data:   <type>
                      - FDDI_802.2
                      - FDDI_SNAP

           Cause:  The IBMFDDIO LAN driver has been loaded previously to
                   support the specified frame type.  The NET.CFG file
                   may contain duplicate FRAME keyword entries for the
                   IBMFDDIO LAN driver.  The IBMFDDIO LAN driver did not
                   load.

           Action: Check the NET.CFG file for 2 FRAME keywords that have
                   the same frame type for the IBMFDDIO LAN driver as
                   specified in this message, but that are in different MLID
                   Section Headings.  If duplicate entries exist, change one
                   of the FRAME keywords.  Valid frame type parameters for
                   the IBMFDDIO LAN driver can be found in
                   "Configurable IBMFDDIO LAN Driver Parameters."

                   If duplicate entries do not exist in the NET.CFG
                   file, then the IBMFDDIO LAN driver was previously
                   loaded from either the command line or the NET.CFG
                   file with the FRAME keyword frame type specified
                   in this error message.  No action is necessary.


  IBMFDDIO-xx-016: The node address was incorrectly specified in the NET.CFG.

           Cause:  The NODE ADDRESS keyword specified in the NET.CFG file
                   for the IBM FDDI Adapter is an incorrect adapter
                   node address.  The node address specified has either
                   the group address bit set or the locally administered
                   address bit not set.  The node address was corrected
                   and the IBMFDDIO LAN driver was loaded.

           Action: Correct the NODE ADDRESS keyword parameter in the
                   NET.CFG file to specify a correct locally administered
                   address according to the IBM TOKEN-RING NETWORK
                   ARCHITECTURE REFERENCE.


  IBMFDDIO-xx-017: An invalid keyword was specified in the NET.CFG on line
                   <xxx>.

           Variable Data:   <xxx> -
                   Decimal value of the line number in the NET.CFG file.

           Cause:  The keyword specified on line xxx in the NET.CFG file
                   is incorrect.  The IBMFDDIO LAN driver was loaded.

           Action: Correct the keyword specified on line xxx of the NET.CFG
                   file to a valid keyword.  Refer to the appropriate Novell


                                  ODI for FDDI, Version 1.0   June 26, 1992  21






                   NetWare manual listed below for information about
                   NET.CFG file keywords.

                   For DOS:
                     NOVELL NETWARE ODI SHELL FOR DOS

                   For OS/2:
                     NOVELL NETWARE REQUESTER FOR OS/2


  IBMFDDIO-xx-018: The frame type specified in the NET.CFG is not supported.

           Cause:  The frame type specified for the FRAME keyword in
                   an IBMFDDIO MLID Section Heading of the NET.CFG file
                   is not supported.

           Action: Edit the NET.CFG file and specify a valid frame type
                   parameter for the FRAME keyword in the MLID Section
                   Heading for the IBMFDDIO LAN driver.  Refer to the
                   appropriate Novell NetWare manual listed below for
                   information about editing a NET.CFG file, and to
                   "Configurable IBMFDDIO LAN Driver Parameters"
                   for information about valid NET.CFG file parameters for
                   the IBMFDDIO LAN driver.

                   For DOS:
                     NOVELL NETWARE ODI SHELL FOR DOS

                   For OS/2:
                     NOVELL NETWARE REQUESTER FOR OS/2


  IBMFDDIO-xx-019: An invalid FDDI node address is specified in NET.CFG.
                   The MLID modified the incorrect address bits.

           Cause:  The NODE ADDRESS keyword specified in the NET.CFG file
                   for the IBM FDDI Adapter is an incorrect adapter node
                   address.  The IBMFDDIO LAN driver did not load.

           Action: Correct the NODE ADDRESS keyword parameter in the
                   NET.CFG file to specify a correct locally administered
                   address according to the IBM TOKEN-RING NETWORK
                   ARCHITECTURE REFERENCE.


  IBMFDDIO-xx-020: This version of the statistics table is not supported.

           Cause:  The version level of the statistics table for the IBMFDDIO
                   LAN driver is not supported.  The IBMFDDIO LAN driver did
                   not load.

           Action: Try to load the IBMFDDIO LAN driver again.  If this
                   error persists, reinstall the IBMFDDIO LAN driver.
                   See "IBMFDDIO LAN Driver Installation Procedure"


                                  ODI for FDDI, Version 1.0   June 26, 1992  22






                   for installation instructions.  Load the IBMFDDIO LAN
                   driver again.  If this error still persists, contact your
                   network administrator or IBM support center.


  IBMFDDIO-xx-021: Could not add MLID Protocol ID.

          Cause:  The LSL is configured with resources for a set number of
                  Protocol Identifiers (default is 4).  This number has been
                  exceeded.

          Action: Edit the NET.CFG file and add the MAX STACKS keyword to
                  reflect the number of boards to be loaded.  Unload the driver
                  and then reload it.

                  example of NET.CFG

                  .
                  .
                  .
                  LINK SUPPORT
                          MAX STACKS 6
                  .
                  .
                  .


                  Refer to the, NOVELL NETWARE ODI SHELL FOR DOS or
                  NOVELL NETWARE REQUESTER FOR OS/2, manual for
                  information on the NET.CFG file.


  IBMFDDIO-xx-022: Could not allocate memory.  Virtual board did not load.

          Cause:  Cannot get enough memory from the system to load another
                  virtual board.

          Action: Do one of the following:
                  1) Install more system memory in the machine.
                  2) Edit the CONFIG.SYS file and remove drivers that are
                     not needed.


  IBMFDDIO-xx-024: The MSM is unable to parse a required custom keyword.

           Cause:  The value entered for a required custom keyword is
                   incorrect.

           Action: Check the values for specified custom keyword when
                   the IBMFDDIO LAN driver was loaded.  Correct keyword
                   values that are incorrect, and then reload the
                   IBMFDDIO LAN driver.




                                  ODI for FDDI, Version 1.0   June 26, 1992  23






  IBMFDDIO-xx-050: The board cannot be found.

           Cause:  There is no IBM FDDI Adapter installed in this computer.
                   The IBMFDDIO LAN driver did not load.

           Action: Install an IBM FDDI Adapter in this computer if it has
                   a 80386 or higher microprocessor, and then reload the
                   IBMFDDIO LAN driver.


  IBMFDDIO-xx-056: This interrupt is already used and cannot be shared.

           Cause:  The interrupt level configured for the IBM FDDI Adapter
                   with the reference diskette cannot be set.  The IBMFDDIO
                   LAN driver for DOS and OS/2 workstations cannot share the
                   same interrupt level with other hardware adapters or
                   device drivers.

           Action: Run the reference diskette for your computer and check
                   that the interrupt level specified for the IBM FDDI
                   Adapter does not conflict with other hardware adapters
                   installed in your computer.  If it does, change the
                   configured interrupt level for the IBM FDDI Adapter to
                   a value that does not conflict with any other hardware
                   adapters installed in your computer.

  IBMFDDIO-xx-071: The matching virtual adapter could not be found.

           Cause:  An error occurred while trying to load another copy
                   of the IBMFDDIO LAN driver to support an additional
                   frame type (FRAME= parameter) on an IBM FDDI Adapter.
                   The MSM could not find a previous copy of the IBMFDDIO
                   LAN driver require to load the specified frame type.

           Action: Obtain the most current copy of the MSM.NLM or
                   MSM311.NLM (if running NetWare version 3.11) and then
                   reload the IBMFDDIO LAN driver for the desired frame
                   types.  If this error persists, contact your network
                   administrator or IBM support center.  Refer to the
                   NOVELL NETWARE SYSTEM ADMINISTRATION manual for
                   information about loading and unloading LAN drivers.


  IBMFDDIO-xx-072: A resource tag is unavailable.

           Cause:  The NetWare Operating system was unable to allocate
                   memory for a resource tag.  The IBMFDDIO LAN driver
                   did not load because required internal resources
                   were not available.  There may be too many NetWare
                   Loadable Modules (NLMs) running in the NetWare Server.

           Action: Unload the NLMs that are loaded but are not being used,
                   and then load the IBMFDDIO LAN driver.  If this error
                   persists, take down and restart the server.  Load the


                                  ODI for FDDI, Version 1.0   June 26, 1992  24






                   IBMFDDIO LAN driver before loading NLMs, this may require
                   you to edit the AUTOEXEC.NCF file before restarting the
                   server.  Refer to NOVELL NETWARE SYSTEM ADMINISTRATION for
                   information about the AUTOEXEC.NCF file.


  IBMFDDIO-xx-073: Unable to allocate memory.

           Cause:  The NetWare Operating system was unable to allocate
                   memory for the IBMFDDIO LAN driver.  The IBMFDDIO
                   LAN driver did not load.

           Action: Unload the NetWare Loadable Modules (NLMs) that are
                   loaded but are not being used, and then load the IBMFDDIO
                   LAN driver.  If this error persists, take down and
                   restart the server.  Load the IBMFDDIO LAN driver before
                   loading NLMs; this may require you to edit the
                   AUTOEXEC.NCF file before restarting the server.  Refer to
                   NOVELL NETWARE SYSTEM ADMINISTRATION for information
                   about the AUTOEXEC.NCF file.


  IBMFDDIO-xx-074: The hardware interrupt cannot be set.

           Cause:  The NetWare Operating system was unable to set the
                   hardware interrupt level requested by the IBMFDDIO
                   LAN driver.  The IBMFDDIO LAN driver did not load.

           Action: Try to load the IBMFDDIO LAN driver again.  If the error
                   persists, contact your network administrator or IBM
                   support center.


  IBMFDDIO-xx-075: The MLID cannot be registered with the LSL.

           Cause:  The IBMFDDIO LAN driver could not be registered with the
                   Link Support Layer (LSL) module.  The maximum number of
                   LAN drivers are already loaded or there was not enough
                   memory to load the IBMFDDIO LAN driver.  The IBMFDDIO
                   LAN driver did not load.

           Action: Unload LAN drivers that are not being used and then
                   load the IBMFDDIO LAN driver.  If this error persists,
                   take down and restart the server.  Load the IBMFDDIO LAN
                   driver before loading other LAN drivers; this may require
                   you to edit the AUTOEXEC.NCF file before restarting the
                   server.  Refer to NOVELL NETWARE SYSTEM ADMINISTRATION for
                   information about the AUTOEXEC.NCF file.


  IBMFDDIO-xx-076: The polling procedure cannot be added.

           Cause:  There are too many polling processes registered with
                   the NetWare Operating system.  The IBMFDDIO LAN


                                  ODI for FDDI, Version 1.0   June 26, 1992  25






                   driver did not load.

           Action: Unload LAN drivers or NetWare Loadable Modules that
                   are loaded but are not being used.  Try to load the
                   IBMFDDIO LAN driver again.  If this error persists,
                   contact your network administrator or IBM support
                   center.


  IBMFDDIO-xx-077: The event notification routine cannot be registered.

           Cause:  The NetWare Operating system was unable to allocate
                   memory to register the IBMFDDIO LAN driver event
                   notification routine.  The IBMFDDIO LAN driver did
                   not load.

           Action: Unload LAN drivers or NetWare Loadable Modules that
                   are loaded but are not being used.  Try to load the
                   IBMFDDIO LAN driver again.  If this error persists,
                   contact your network administrator or IBM support
                   center.


  IBMFDDIO-xx-126: The group bit in the node address override was cleared.

           Cause:  The address specified for the node address parameter
                   is an incorrect adapter node address.  The node
                   address specified had the group address bit set.
                   The group address bit was cleared by the IBMFDDIO
                   LAN driver.  The IBMFDDIO LAN driver was loaded.

           Action: Correct the node addres parameter to specify a locally
                   administered address according to the IBM TOKEN-RING
                   NETWORK ARCHITECTURE REFERENCE.  On a DOS or
                   OS/2 Workstation change the node address parameter in
                   the NET.CFG file.  On a NetWare Server change the node
                   address parameter specified on the command line when the
                   IBMFDDIO LAN driver was loaded or change the node address
                   specified in the IBMFDDIO.CFG configuration file.


  IBMFDDIO-xx-078: The firmware file cannot be read.

           Cause:  The Netware Operating system was unable to load the
                   IBMFDDIO LAN driver.  The IBMFDDIO LAN driver was not
                   loaded.

           Action: Obtain another copy of the IBMFDDIO LAN driver from
                   the original distribution diskette.  Reload the IBMFDDIO
                   LAN driver.  If this error persists, contact you network
                   network administrator or IBM support center.


  IBMFDDIO-xx-084: Unable to allocate memory below 16 Megabyte boundary.


                                  ODI for FDDI, Version 1.0   June 26, 1992  26






           Cause:  The Netware Operating system ran out of memory buffers
                   below 16 megabytes.  The IBMFDDIO LAN driver was not
                   loaded.

           Action: Set the Reserved Buffers Below 16 Meg parameter in the
                   STARTUP.NCF to a larger number.


  IBMFDDIO-xx-086: The driver parameter block is too small.

           Cause:  The IBMFDDIO.LAN file is designed to run with an older
                   version of the MSM.NLM.  The IBMFDDIO LAN driver was
                   not loaded.

           Action: Obtain an older version of the MSM.NLM or a newer
                   version of the IBMFDDIO.LAN file.


  IBMFDDIO-xx-087: The media parameter block is too small.

           Cause:  The FDDITSM.NLM NetWare Loadable Module (NLM) is
                   designed to run with an older version of the MSM.NLM
                   or MSM311.NLM if running NetWare version 3.11.

           Action: Obtain an older version of the MSM.NLM (MSM311.NLM
                   if running NetWare version 3.11) or a new version of
                   the FDDITSM NLM.


  IBMFDDIO-xx-091: The hardware configuration conflicts.

           Cause:  The IBMFDDIO LAN driver requested use of a hardware
                   resource that was already being used by another
                   hardware device.  The IBMFDDIO LAN driver did not load.

           Action: Change the hardware configuration of the IBM FDDI
                   Adapter or the hardware configuration of the
                   conflicting hardware device.


  IBMFDDIO-xx-092: Cannot schedule AES without an HSM routine.

           Cause:  The IBMFDDIO.LAN file is damaged.

           Action: Obtain another copy of the IBMFDDIO LAN driver from
                   the original distribution diskette.  Reload the IBMFDDIO
                   LAN driver.  If this error persists, contact you network
                   network administrator or IBM support center.


  IBMFDDIO-xx-093: Cannot schedule interrupt time call back without an
                   HSM routine.



                                  ODI for FDDI, Version 1.0   June 26, 1992  27






           Cause:  The IBMFDDIO.LAN file is damaged.


           Action: Obtain another copy of the IBMFDDIO LAN driver from
                   the original distribution diskette.  Reload the IBMFDDIO
                   LAN driver.  If this error persists, contact you network
                   network administrator or IBM support center.


  IBMFDDIO-xx-094: Cannot set hardware interrupt witout an HSM routine.

           Cause:  The IBMFDDIO.LAN file is damaged.

           Action: Obtain another copy of the IBMFDDIO LAN driver from
                   the original distribution diskette.  Reload the IBMFDDIO
                   LAN driver.  If this error persists, contact you network
                   network administrator or IBM support center.


  IBMFDDIO-xx-095: Cannot add polling without an HSM routine.

           Cause:  The IBMFDDIO.LAN file is damaged.

           Action: Obtain another copy of the IBMFDDIO LAN driver from
                   the original distribution diskette.  Reload the IBMFDDIO
                   LAN driver.  If this error persists, contact you network
                   network administrator or IBM support center.


  IBMFDDIO-xx-127: The local bit in the node address override was set.

           Cause:  The address specified for the node address parameter
                   is an incorrect adapter node address.  The node address
                   specified does not have the locally administered address
                   bit set.  The locally administered address bit was set
                   by the IBMFDDIO LAN driver.  The IBMFDDIO LAN driver was
                   loaded.

           Action: Correct the node address parameter to specify a locally
                   administered address according to the IBM TOKEN-RING
                   ARCHITECTURE REFERENCE.  On a DOS or OS/2
                   Workstation change the node address parameter in the
                   NET.CFG file.  On a NetWare Server change the node
                   address parameter specified on the command line when the
                   IBMFDDIO LAN driver was loaded or change the node address
                   specified in the IBMFDDIO.CFG configuration file.


  IBMFDDIO-xx-200: Initializing the IBM FDDI Adapter ... please wait.

           Cause:  The IBM FDDI Adapter initialization process (resetting
                   the adapter and downloading the adapter microcode) can take
                   up to 30 seconds.



                                  ODI for FDDI, Version 1.0   June 26, 1992  28






           Action: None.


  IBMFDDIO-xx-201: Inserting the IBM FDDI Adapter into the ring.

           Cause:  The IBMFDDIO LAN driver is waiting for the IBM FDDI
                   Adapter to insert into the ring.

           Action: None.


  IBMFDDIO-xx-202: The IBM FDDI Adapter could not insert into the ring.

           Cause:  The IBM FDDI Adapter did not insert into the ring within
                   the timeout value.  This is normal if there are no other
                   stations on the ring.  If there are other stations on the
                   ring, and the adapter did not insert, contact your network
                   administrator.

           Action: This condition should correct itself when a second
                   station inserts into the ring.  If another station
                   inserts and this condition does not correct itself,
                   contact your network administrator or IBM support center.


  IBMFDDIO-xx-203: The IBMFDDIO LAN driver and IBM FDDI Adapter require a
                   computer with at least an 80386 microprocessor.

           Cause:  The IBM FDDI Adapter must be installed in a computer
                   that has a 80386 or higher microprocessor.  The IBMFDDIO
                   LAN driver did not load.

           Action: Install the adapter in a computer with a 80386 or higher
                   microprocessor, and reload the IBMFDDIO LAN driver.


  IBMFDDIO-xx-204: The IBM FDDI Adapter requires a computer with a Micro
                   Channel bus.

           Cause:  The IBM FDDI Adapter will work only in a computer that
                   supports the IBM Micro Channel Architecture.

           Action: Install the IBM FDDI Adapter and IBMFDDIO LAN driver
                   in a computer that supports the IBM Micro Channel
                   Architecture.


  IBMFDDIO-xx-205: The IBMFDDIO LAN driver was not loaded because of an
                   incorrect keyword value.

           Cause:  The value for one of the keywords specified on the
                   command line or in the IBMFDDIO.CFG file was not within
                   the allowable range.  The IBMFDDIO LAN driver did not
                   load.


                                  ODI for FDDI, Version 1.0   June 26, 1992  29






           Action: Correct the value of the keyword displayed in the
                   message that was displayed above this error message, and
                   reload the IBMFDDIO LAN driver.


  IBMFDDIO-xx-206: The IBMFDDIO LAN driver was not loaded because of an
                   incorrect keyword value in the NET.CFG file.

           Cause:  The value for one of the keywords specified in the
                   NET.CFG file was not within the allowable range.  The
                   IBMFDDIO LAN driver did not load.

           Action: Correct the value for the keyword displayed in the
                   message that was displayed above this error message, and
                   reload the IBMFDDIO LAN driver.


  IBMFDDIO-xx-207: The IBM FDDI Adapter could not be reset.

           Cause:  The IBMFDDIO LAN driver timed out while waiting for the
                   IBM FDDI Adapter to complete a hardware reset.  The
                   IBMFDDIO LAN driver did not load.

           Action: Restart your computer and try to load the IBMFDDIO LAN
                   driver again.  If this error persists, contact your
                   network administrator or IBM support center.


  IBMFDDIO-xx-208: The IBM FDDI Adapter microcode file, IBMFDDI.BIN,
                   could not be loaded.

           Cause:  A checksum error occurred when the IBMFDDIO LAN driver
                   tried to load the IBM FDDI Adapter microcode file,
                   IBMFDDI.BIN.

           Action: Reinstall the IBMFDDIO LAN driver and the adapter
                   microcode file, IBMFDDI.BIN, and restart the computer.
                   If the error persists, contact your IBM support center or
                   place of purchase.


  IBMFDDIO-xx-209: The IBMFDDIO LAN driver failed to initialize the
                   IBM FDDI Adapter.

           Cause:  There was a problem while initializing the IBM FDDI
                   Adapter.  There may be previous error messages
                   above this one or the IBM FDDI Adapter may not be
                   responding.

           Action: Correct any problems with error messages displayed
                   above this error message, and then reload the IBMFDDIO
                   LAN driver.



                                  ODI for FDDI, Version 1.0   June 26, 1992  30






                   If this is the only error message that is displayed,
                   restart your computer and check the adapter by running
                   the adapter diagnostic tests located on the Option
                   Diskette that was shipped with the IBM FDDI Adapter.
                   Then, reload the IBMFDDIO LAN driver.  If this error
                   persists, contact your network administrator or IBM
                   support center.


  IBMFDDIO-xx-210: Could not find an IBM FDDI Adapter in this computer.

           Cause:  There is no IBM FDDI Adapter installed in this computer.
                   The IBMFDDIO LAN driver did not load.

           Action: Install an IBM FDDI Adapter in this computer if it has
                   a 80386 or higher microprocessor, and then reload the
                   IBMFDDIO LAN driver.


  IBMFDDIO-xx-211: The IBM FDDI Adapter was not found in the slot
                   specified in the NET.CFG file.

           Cause:  There is no IBM FDDI Adapter in the slot specified by the
                   SLOT keyword in the NET.CFG file.

           Action: Correct the SLOT keyword so that it indicates a slot
                   number in which an IBM FDDI Adapter is located, and then
                   reload the IBMFDDIO LAN driver.

                   If you do not include a SLOT keyword, the IBMFDDIO LAN
                   driver will default to using the first IBM FDDI Adapter
                   it finds.

                   If there is an IBM FDDI Adapter in the specified slot,
                   contact your network administrator or IBM support center.


  IBMFDDIO-xx-212: Insufficient memory available for configured transmit and
                   receive buffers.

           Cause:  During initialization of the IBMFDDIO LAN driver, there
                   was insufficient memory available for the configured
                   number of transmit and receive buffers.

           Action: (Server)
                   Increase the number of buffers that the server operating
                   system can allocate by editing the STARTUP.NCF file on
                   the server.  Increase the Minimum Packet Receive Buffers
                   server parameter in the STARTUP.NCF file by the total
                   number of transmit and receive buffers that the IBMFDDIO
                   LAN driver is using.  Take down, and then restart the
                   NetWare Server.

                   If this error persists, unload the LAN drivers and


                                  ODI for FDDI, Version 1.0   June 26, 1992  31






                   NetWare Loadable Modules (NLMs) that are loaded but are
                   not being used at the NetWare Server.

                   (OS/2 Workstation)
                   Increase the number of buffers that are allocated by
                   the Link Support Layer (LSL.SYS) when it is loaded by
                   editing or creating a NET.CFG file.  Under the Link
                   Support heading in the NET.CFG file, increase the first
                   value of the BUFFERS parameter by the total number of
                   transmit and receive buffers that the IBMFDDIO LAN
                   driver is using.  Restart your computer.

                   See "Sample NET.CFG Configuration File for DOS and OS/2
                   Workstations" for a sample NET.CFG file.

                   (All Platforms)
                   If this error still persists, decrease the number of
                   buffers that are being used by the IBMFDDIO LAN driver
                   by specifying the transmit and receive keywords for the
                   IBMFDDIO LAN driver.

                   See "Configurable IBMFDDIO LAN Driver Parameters"
                   for information about specifying keywords for the
                   operating system that you are using.


    IBMFDDIO-xx-213: A dual attached station was configured as a single
                     attached station.

             Cause:  The IBMFDDIO LAN driver detected both an IBM FDDI Base
                     Adapter/A and an IBM FDDI Extender Adapter/A, which
                     enable this computer to function as a dual attachment
                     station.  However, the ATTACHMENTCLASS parameter is set
                     to 1 for single attachment.

             Action: If you want this computer to remain a single attachment
                     station, no action is necessary.  Otherwise, remove
                     the ATTACHMENTCLASS parameter or change the value to
                     2 for dual attachment.  Reload the IBMFDDIO LAN driver.


  IBMFDDIO-xx-214: A single attached station cannot be configured as a dual
                   attached station.

           Cause:  The IBMFDDIO LAN driver detected only an IBM FDDI Base
                   Adapter/A, so the computer cannot function as a dual
                   attached station.  However, the ATTACHMENTCLASS parameter
                   is set to 2 for dual attachment.  The IBMFDDIO LAN driver
                   did not load.

           Action: Either install an IBM FDDI Extender Adapter/A or change
                   the ATTACHMENTCLASS parameter to 1 for single attachment.
                   Reload the IBMFDDIO LAN driver.



                                  ODI for FDDI, Version 1.0   June 26, 1992  32






  IBMFDDIO-xx-215: The value specified for RXBUFFERS is not valid.  The
                   value has been decreased to the next supported value.

           Cause:  An incorrect value was specified for RXBUFFERS either in
                   the NET.CFG file (for DOS and OS/2), on the command line,
                   or in the IBMFDDIO.CFG file (for the server).  The
                   IBMFDDIO LAN driver used the next lower supported value
                   from the one specified.

           Action: None.  However, to keep this message from being displayed
                   when the IBMFDDIO LAN driver is loaded, change the value
                   specified by the RXBUFFERS keyword to one of the supported
                   values for your operating system.
                   See "Configurable IBMFDDIO LAN Driver Parameters"
                   for the supported values.


  IBMFDDIO-xx-216: The value specified for TXBUFFERS is not valid.  The
                   value has been decreased to the next supported value.

           Cause:  An incorrect value was specified for TXBUFFERS either in
                   the NET.CFG file (for DOS and OS/2), on the command
                   line, or in the IBMFDDIO.CFG file (for the server).  The
                   IBMFDDIO LAN driver used the next lower supported value
                   from the one specified.

           Action: None.  However, to keep this message from being displayed
                   when the IBMFDDIO LAN driver is loaded, change the value
                   specified by the TXBUFFERS keyword to one of the supported
                   values for your operating system.
                   See "Configurable IBMFDDIO LAN Driver Parameters"
                   for the supported values.


  IBMFDDIO-xx-217: The value specified for ATTACHMENTCLASS is not valid.

           Cause:  The value specified for the ATTACHMENTCLASS parameter is
                   incorrect.  The IBMFDDIO LAN driver did not load.

           Action: Specify either 1 for a single attachment station or 2
                   for a dual attachment station, and then reload the
                   IBMFDDIO LAN driver.


  IBMFDDIO-xx-218: The value specified for USERDATA is not valid.

           Cause:  The value specified for the USERDATA parameter is
                   incorrect for one of the following reasons:
                   - Too long
                   - Not enclosed in double quotes.

                   The IBMFDDIO LAN driver did not load.



                                  ODI for FDDI, Version 1.0   June 26, 1992  33






           Action: Remove or correct the USERDATA parameter as described in
                   "Configurable IBMFDDIO LAN Driver Parameters."
                   Reload the IBMFDDIO LAN driver.


  IBMFDDIO-xx-219: The value specified for PMFPASSWORD is not valid.

           Cause:  The value specified for the PMFPASSWORD parameter is
                   incorrect for one of the following reasons:
                   - Too long
                   - Too short
                   - Not enclosed in double quotes.

                   The IBMFDDIO LAN driver did not load.

           Action: Remove or correct the PMFPASSWORD parameter as decribed
                   in "Configurable IBMFDDIO LAN Driver Parameters."
                   Reload the IBMFDDIO LAN driver.


  IBMFDDIO-xx-220: The IBM FDDI Adapter path test failed while inserting.

           Cause:  The adapter performs a test of its various data paths
                   when it is attempting to insert into the ring.  This
                   message indicates that the data path test has failed and
                   that the adapter could not insert into the ring.  If you
                   are running the IBMFDDIO LAN driver on a DOS or OS/2
                   workstation, then the IBMFDDIO LAN driver did not load.

           Action: Restart the computer and try to load the IBMFDDIO LAN
                   driver again.  If the path test continues to fail,
                   check the adapter by running the adapter diagnostic tests
                   located on the Option Diskette that was shipped with the
                   IBM FDDI Adapter.  If there is a problem with the adapter
                   hardware, contact your network administrator or IBM
                   support center.


  IBMFDDIO-xx-221: A disconnect frame was received from a remote station.

           Cause:  The IBM FDDI Adapter received a disconnect frame request
                   that was sent by another FDDI adapter at a remote
                   station.  The IBM FDDI Adapter installed in this
                   computer disconnected from the ring.

           Action: To insert the IBM FDDI Adapter back into the ring,
                   unload the IBMFDDIO LAN driver (for the NetWare Server
                   and DOS workstations) and then reload it.  If this error
                   persists, contact your network administrator or IBM
                   support center.


  IBMFDDIO-xx-222: The IBM FDDI Adapter failed to insert into the ring.



                                  ODI for FDDI, Version 1.0   June 26, 1992  34






           Cause:  The IBM FDDI Adapter was unable to insert into the ring
                   because of an incorrect network configuration.

           Action: Check that the FDDI adapter cable is connected correctly
                   to the IBM FDDI Base Adapter/A.  If you have a dual
                   attached station, check that the FDDI adapter cable is
                   connected correctly to the IBM FDDI Extender Adapter/A.
                   Refer to the hardware installation manual shipped with the
                   IBM FDDI Adapter for information about connecting your IBM
                   FDDI Adapter to the network.

                   Reload the IBMFDDIO LAN driver.  If this error persists,
                   have the network administrator check the network
                   configuration.


  IBMFDDIO-xx-223: The IBM FDDI Adapter failed to insert into the ring;
                   another adapter is using the same node address.

           Cause:  The IBM FDDI Adapter could not insert into the ring
                   because another station is using the same value that was
                   specified for the node address parameter at your station.

           Action: Change the node address parameter value specified for
                   your station.  This parameter is specified as NODE= (at
                   the NetWare Server) or NODE ADDRESS in NET.CFG (at DOS
                   and OS/2 workstations).
                   See "Configurable IBMFDDIO LAN Driver Parameters"
                   for more information about configuration parameters.


  IBMFDDIO-xx-224: Could not open the IBM FDDI Adapter microcode file,
                   IBMFDDI.BIN.

           Cause:  The microcode file, IBMFDDI.BIN, could not be opened by
                   the IBMFDDIO LAN driver.  It is likely that the microcode
                   file is not or was never installed in the same directory
                   as the IBMFDDIO LAN driver.  The IBMFDDIO LAN driver did
                   not load.

           Action: Copy the microcode file, IBMFDDI.BIN, from the adapter
                   diskette shipped with the IBM FDDI Adapter to the file
                   directory where the IBMFDDIO LAN driver is located; then,
                   reload the IBMFDDIO LAN driver.  If this error persists,
                   reinstall the IBMFDDIO LAN driver, and then reload the
                   driver.
                   See "IBMFDDIO LAN Driver Installation Procedure"
                   for installation instructions.

                   If this error persists, contact your IBM support center or
                   place of purchase.


  IBMFDDIO-xx-225: Could not close the IBM FDDI Adapter microcode file,


                                  ODI for FDDI, Version 1.0   June 26, 1992  35






                   IBMFDDI.BIN.

           Cause:  An error occurred when the IBMFDDIO LAN driver attempted
                   to close the microcode file, IBMFDDI.BIN.  This error may
                   indicate a hardware problem with the computer.  The
                   IBMFDDIO LAN driver did not load.

           Action: Reinstall the IBMFDDIO LAN driver and IBMFDDIO.BIN, and
                   then reload the IBMFDDIO LAN driver.
                   See "IBMFDDIO LAN Driver Installation Procedure"
                   for installation instructions.

                   If this error persists, contact your IBM support center or
                   place of purchase.


  IBMFDDIO-xx-226: Could not read the IBM FDDI Adapter microcode file,
                   IBMFDDI.BIN.

           Cause:  An error occurred when the IBMFDDIO LAN driver attempted
                   to read the microcode file, IBMFDDI.BIN.  This error may
                   indicate a hardware problem with the computer.  The
                   IBMFDDIO LAN driver did not load.

           Action: Reinstall the IBMFDDIO LAN driver and IBMFDDIO.BIN, and
                   then reload the IBMFDDIO LAN driver.

                   If this error persists, contact your IBM support center or
                   place of purchase.


  IBMFDDIO-xx-227: Could not set the configured interrupt level for the IBM
                   FDDI Adapter.

           Cause:  The interrupt level configured for the IBM FDDI Adapter
                   with the reference diskette cannot be set.  The IBMFDDIO
                   LAN driver for DOS and OS/2 workstations cannot share the
                   same interrupt level with other hardware adapters or
                   device drivers.

           Action: Run the reference diskette for your computer and check
                   that the interrupt level specified for the IBM FDDI
                   Adapter does not conflict with other hardware adapters
                   installed in your computer.  If it does, change the
                   configured interrupt level for the IBM FDDI Adapter to
                   a value that does not conflict with any other hardware
                   adapters installed in your computer.


  IBMFDDIO-xx-228: A Micro Channel bus error occurred.

           Cause:  An error was detected with the Micro Channel bus while
                   data was being transferred between the IBM FDDI Adapter
                   and the computer.  This condition is reported as an


                                  ODI for FDDI, Version 1.0   June 26, 1992  36






                   alert.

           Action: The adapter will retry the data transfer, and the
                   IBMFDDIO LAN driver MicroChannelError statistics counter
                   will be incremented.

                   If this error persists, check the adapter by running the
                   adapter diagnostic tests located on the Option Diskette
                   that was shipped with the IBM FDDI Adapter, and check your
                   computer by running the hardware diagnostic tests.  If
                   this error still persists, contact your IBM support center
                   or place of purchase of the IBM FDDI Adapter.


  IBMFDDIO-xx-229: The IBM FDDI Adapter reported an adapter check error.

           Cause:  The IBM FDDI Adapter detected an adapter check error.
                   The IBM FDDI Adapter is reset by the IBMFDDIO LAN
                   driver when this error is reported.  This condition
                   is reported as an alert.

           Action: The IBM FDDI Adapter and IBMFDDIO LAN driver may
                   recover from this error.  If the Adapter Check Count
                   continues to increase, check the adapter by running the
                   adapter diagnostic tests located on the Option Diskette
                   that was shipped with the IBM FDDI Adapter.  See
                   "IBM FDDI Adapter Custom Statistic Counters"
                   for information about the Adapter Check Count.  If there
                   are no problems with the adapter, reload the IBMFDDIO LAN
                   driver.


  IBMFDDIO-xx-230: The IBM FDDI Adapter failed a diagnostic test.

           Cause:  The IBM FDDI Adapter failed a diagnostic test
                   when the adapter was reset.  This condition is
                   reported as an alert.

           Action: The IBM FDDI Adapter and IBMFDDIO LAN driver may
                   recover from this error.  If the Adapter Diagnostic Count
                   continues to increase, check the adapter by running the
                   adapter diagnostic tests located on the Option Diskette
                   that was shipped with the IBM FDDI Adapter.  See
                   "IBM FDDI Adapter Custom Statistic Counters"
                   for information about the Adapter Diagnostic Count.  If
                   there are no problems with the adapter, reload the
                   IBMFDDIO LAN driver.


  IBMFDDIO-xx-231: The IBM FDDI Adapter alert condition was corrected.

           Cause:  The IBM FDDI Adapter and IBMFDDIO LAN driver have
                   recovered from a previously reported alert condition.



                                  ODI for FDDI, Version 1.0   June 26, 1992  37






           Action: None.























































                                  ODI for FDDI, Version 1.0   June 26, 1992  38